## Slide 1: Physical Market Structures: CRUDE, Natural Gas, Power & NG Liquids

## Slide 3: Supply & demand revolution

## Slide 4: North American Producing Basins
Notes: Natural gas resources are distributed between a number of major geologic basins. Most U.S. natural gas is produced in the onshore and offshore regions of the Gulf coast. According to 2001 data, 60 percent of gas produced in the United States flows from the onshore and offshore areas of the Gulf of Mexico. Another 23 percent was produced in New Mexico, Oklahoma, and Wyoming.
Many major consuming markets (e.g., the Northeast, Midwest, California, and Florida) are located at significant distances away from the producing regions, so the system depends on the pipeline network.
The interstate pipeline network consists of almost 300,000 miles of pipe.
(The map shows major geologic basins and transportation corridors. The relative size of transportation flows is reflected in the size of the arrows. The basins, on the other hand, are represented in terms of the area in which the basins lie. The largest basins on the map are not necessarily the most prolific.)

## Slide 5: Supply Revolution

## Slide 7: Could this have been predicted 5 years ago?

## Slide 8: Crude Oil

## Slide 9: PADD Locations

## Slide 10: Crude Oil Spreads
Geographic Region | Crude Oil | API Weight | Sulfur Content (%) | Average 2008 Price | Average 2011 Price
North Sea |  |  |  |  | 
 | Dated Brent | 38.5 | 0.40 | 97.69 | 111.05
 | Oseberg | 35.4 | 0.26 | 99.87 | 113.01
 | Ekofisk | 42.3 | 0.15 | 97.69 | 112.83
West Africa |  |  |  |  | 
 | Bonny Light | 34.5 | 0.10 | 97.69 | 113.53
 | Cabinda | 32.5 | 0.13 | 94.59 | 110.45
Mediterranean |  |  |  |  | 
 | Iran Heavy | 31.0 – 32.0 | 1.80 | 89.77 | 106.57
 | Iran Light | 33.5 – 34.0 | 1.40 | 94.15 | 108.07
Persian Gulf |  |  |  |  | 
 | Dubai | 31.2 | 2.01 | 93.97 | 106.15
 | Oman | 37.0 | 1.08 | 99.54 | 106.66

## Slide 11: Crude Oil Spreads
Geographic Region | Crude Oil | API Weight | Sulfur Content (%) | Average 2008 Price | Average 2011 Price
Australia |  |  |  |  | 
 | Cossack | 49.0 | 0.04 |  | 
 | Gippsland | 48.0 | 0.10 |  | 
 | Griffin | 55.0 | 0.03 |  | 
China |  |  |  |  | 
 | Daqing | 32.7 | 0.10 | 92.41 | 117.45
Indonesia |  |  |  |  | 
 | Attaka | 44.7 | 0.04 | 101.14 | 121.46
 | Widuri | 33.3 | 0.07 |  | 
United States |  |  |  |  | 
 | (WTI) | 38.0 – 40.0 | 0.30 | 99.92 | 95.05
 | (WTS) | 33 | 0.16 | 96.15 | 93.00

## Slide 12: Light/Heavy Spread
Chart: Light / Heavy Spread
Source: S&P’s DRI/Platts
Notes: The light-heavy crude oil price difference can fluctuate quite a bit in the short term. However, this graph shows that, while there are some significant cyclical ups and downs, there is no sign of increasing differentials trendwise.
That is, as yet, there is no sign of a major shift to heavy crude oil advantage relative to history.
But will this continue in to the future?
Updated 9/29/2010

## Slide 13: Light/Heavy Spread
Chart: Light/ Heavy Spread

## Slide 14: WTI / Brent Spread: The Bakken Shale

## Slide 15: WTI / Brent Spread has helped PADD II & PADD III Refineries / Hurt PADD I

## Slide 16: Natural Gas

## Slide 17: General Factors Affecting Natural Gas
Demand Shock:
  2008 Recession decrease natural gas consumption to 1998 levels
  Lower 48 currently consuming approximately 55 BCF / D
Supply Shock:
  Natural gas domestic production has increased 10% during that time
    2008 Daily Production – 45 BCF /D
    2011 Daily Production – 55 BCF / D
  Reasons:
    Shale & horizontal drilling technology
    North American Reserves have skyrocketed
  Shale drilling being driven by liquids prices, not NG prices

## Slide 18
Two Eras: Natural Gas Price Chart
Notes: (These prices are based on weekly samples.)
What caused the spike in early 2002? War in Iraq.
Not updated - bloomberg

## Slide 19
Year Natural Gas Price Chart

## Slide 20
Natural Gas Historical Volatility
Notes: Volat was calced based on 30 days of data and then ann’zed by mult by sqrt 252.
Not updated - bloomberg

## Slide 21
Natural Gas Historical Volatility

## Slide 22: Natural Gas Storage Effects, May 2012

## Slide 23: Natural Gas Demand Changes (2015)
Coal Plant Retirement
Commercial Demand
  North American feedstock will be lowest in world with the exception of Qatar
  Manufacturing Boom
  Chemicals Boom
Residential / Commercial Demand
  Replacing less green (heating oil) boilers with natural gas boilers
  Housing overhang being worked though
LNG Export
  At $6/mmBTU
    LNG to Asia: $10 / mmBTU
    Asian Price - $85/mmBTU
CNG Vehicles

## Slide 24: Natural Gas Liquids (NGL)

## Slide 25: Historic NGL Pricing
Chart: 
Notes: Not updated - bloomberg

## Slide 27: Natural Gas Liquids: Supply Areas
Notes: Unlike the interstate natural gas market, all of these subregions are both supply and demand areas.
Mention PJM & COB.

## Slide 30: NGL Market Hubs
Edmonton/Fort Saskatchewan, Alberta
Sarnia, Ontario
Conway, Kansas
Mont Belvieu, Texas
  Because of physical infrastructure, Mon Belvieu acts as a “price setter” for the other three regions

## Slide 31: NGL Pricing
Most contracts are priced as an index to one of the four locations
NGL prices typically track/follow crude oil prices.
  Ethane is the exception tracking natural gas prices
  Propane trades near 75% to crude oil
  Butane trades near 85% to crude oil
  These relationships change as natural gas prices trade high in relation to crude oil prices (2000 – 2001)
    NGL processors will sell the heavier components in the natural gas when natural gas prices are high

## Slide 32: NGLs provide a significant revenue boost to NG
Source: EIA, company reports, Barclays Capital equities and commodities research
NGLs price, % of WTI
Comparing well revenues
Price for Haynesville well
to match Eagle Ford

## Slide 33: Associated gas: Eagle Ford
33
Production from oil window (MMcfe/d)
Production from liquids window (MMcfe/d)
___________________________
Source: The Railroad Commission of Texas, company reports, Barclays Research
Gas production by source (MMcf/d)
Eagle Ford gas rig count

## Slide 34: Electricity

## Slide 35: Power: Major Regions
Source: http://www.nerc.com
Notes: Unlike the interstate natural gas market, all of these subregions are both supply and demand areas.
Mention PJM & COB.

## Slide 36: Regional Power & Coal Markets (2012)

## Slide 37: Power Supply = Market Areas
Differing Prices & Low Price Correlation Across Regions.
Note that this explains why basis swaps are not common in power trading.
Transmission
Constraints
Between
Regions
Different
Supply
Cost & Mix
Across
Regions
Notes: Arbitrage opportunities across regions are often very temporary, even if price discrepancies remain.
Is anything common in power trading?

## Slide 38
Intra-Region Basis Prices
Source: http://www.pjm.com/documents/maps/pjm-zones.pdf
Notes: Within MAAC is the PJM Regional Transmission Organization (RTO). Prices vary even within PJM such as the PJM East vs PJM West price quotes.

## Slide 39: Electricity Issues
Green Power has not worked
Conversion to Natural Gas
  Decommission of Coal Plants
  Conversion to Natural Gas
  What happens when gas prices increase?
Capacity markets
Hub transmission markets
Price Caps

## Slide 40: Annual average boost to gas consumption via coal displacement (vs. 2008 base year)
40
___________________________
Source: EIA, Barclays Capital.
Bcf/d
~10% loss in coal market share since 2008
~10% of total gas consumption

## Slide 41: At what price does gas compete with coal? (Gas-equivalent prices and volume of all coal in the US, October 2011 data, includes transportation costs)
41
___________________________
Source: Barclays Capital.
Current gas price
2011 gas prices
2010 gas prices

## Slide 42: Negative margins weigh on coal plant retirement decisions (un-contracted coal plants)
42
___________________________
Source: ICE, Platts, CME, Barclays Capital.
Mid-Atlantic power market cash
coal plant margins, $/MWh
Falling forward gas prices challenge
coal, $/MMBtu (incl. transport costs)
Western US coal plant margins,
$/MWh (2013-2014)
Eastern US coal plant margins,
$/MWh (2013-2014)

## Slide 43: Physical Markets
Regional for all commodities
Price differentials occur via location
Arbitrages can occur from short term demand spikes
Arbitrages can occur between physical and financial markets